Sector Processor to Detector Dependent Unit Interface

Petersburg Nuclear Physics Institute / University of Florida

Version 1.1

October 18, 2001

# Introduction

The Sector Processor (SP) reconstructs tracks from the track segments delivered by the Muon Port Cards (MPC) and the Drift Tube (DT) Track-Finder. The SP decision on tracks is passed to the Muon Sorter (MS), and eventually to the Muon and Global Trigger for further processing. The SP stores all incoming MPC data along with reconstructed tracks in a FIFO buffer for a time sufficient to receive the corresponding L1 Accept. Upon receiving L1A the input and output SP data are combined into the Event Frame and transmitted to the Detector Dependent Unit (DDU) via optical link running at 1.6GBPS. The SP uses a Texas Instruments TLK2501 Transmitter to feed fiber optics with a serialized data stream converted from the 16-bit @ 80 MHz parallel input. Two control signals Transmit Enable (TX_EN) and Transmit Error coding (TX_ER) define four possible modes of Transmitter operation, Table 1.

Table 1. Transmit Data Controls

| TX_EN | TX_ER | ENCODED 20-BIT DATA |
| --- | --- | --- |
| Low | Low | Idle <K28.5, D5.6>, = 0xBCC5 <K28.5, D16.2> = 0xBC50 |
| Low | High | Carrier extend <K23.7, K23.7> = 0xF7F7 |
| High | Low | Normal data character <DX.Y> |
| High | High | Transmit error propagation <K30.7, K30.7> = 0xFEFE |

Each valid Transmission Character of the 8B/10B Transmission Code is given a name using the following convention: Cxx.y, where C is used to show whether the Transmission Character is a Data Character (C is set to D) or an Extended Character (C is set to K). There are 256 valid Transmission Data Characters and 12 valid Extended Characters [].

The DDU uses the same part to deserialize incoming data and convert it back into 16-bit @ 80 MHz parallel words. The DDU stores incoming data in the 18-bit wide input FIFO, if only the TLK2501 Receive Data Valid / Loss of Signal (RX_DV/LOS) output is High, Table 2. The stored data is 16-bit Receive Data bus (RXD), RX_DV/LOS and Receive Error (RX_ER) outputs [].

Table 2. Receive Status Signals

| RECEIVED 20-BIT DATA | RX_DV/LOS | RX_ER |
| --- | --- | --- |
| Idle ( < K28.5, D5.6>, = 0xBCC5 < K28.5, D16.2> = 0xBC50) | Low | Low |
| Carrier extend (K23.7, K23.7) = 0xF7F7 | Low | High |
| Normal data character (DX.Y) | High | Low |
| Receive error propagation (K30.7, K30.7) = 0xFEFE | High | High |

# Frames

The SP sends data to the DDU using an ordered set of 16-bit words called Frames. A Frame is composed of a Start-of-Frame (SOF) delimiter, frame content, and an End-of-Frame (EOF) delimiter, Table 3. The SP uses the TLK2501 Controls to build Frames. Inserting a Frame in the sequence of Idles performs frame transmission. Idles are transmitted immediately upon completion of the Frame, and may be transmitted anywhere inside Frame (see exception below).

Basically there are two types of Frames: Event Frames (EF) and Fast Monitoring Frames (FMF). The SP provides the DDU with Fast Monitoring (FM) data, which is transmitted either as a part of the Event Frame or as a dedicated FMF. If the trigger rate is high enough, the SP sends only EFs to the DDU. Each EF carries the Fast Monitoring (FM) data in its EOF. If L1A rate drops below 10 KHz and/or there are changes in the SP status to be reported to the Fast Monitoring system, the SP initiates transmission of the FMF.

The DDU processes Event Frames and Fast Monitoring Frames differently. It extracts the Fast Monitoring data out of the Event Frame and passes it to the Fast Monitoring Module (FMM), while sending the entire Event Frame further downstream for data logging. The Fast Monitoring data from the Fast Monitoring Frame is intended exclusively for the FMM use. The FMF is not supposed to be logged to disk.

Table 3: Frame Structure

| Frame Structure | Comment |
| --- | --- |
| SOF | Start-of-Frame |
| Data | Frame content |
| ----- | ------------ |
| ----- | ------------ |
| Data | Frame content |
| EOF | End-of-Frame |

## Start-of-Frame

The Start-of-Frame delimiter precedes the frame content. The Start-of-Frame delimiter is composed of two immediately following 16-bit words, Table 4:

- The Error propagation word <K30.7, K30.7> or 0xFEFE

- The SP Identifier and Frame Type word.

No Idles are allowed between SOF words. The SP ID is a 5-bit SP Geographical Address and the Frame Type is either zero for Fast Monitoring Frames (FMF), or non-zero for Event Frames (EF)

Table 4: Start-of-Frame Delimiter Structure

| Word | TX_EN | TX_ER | TXD | RX_DV/ LOS | RX_ER | RXD | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| SOF1 | High | High | 0xXXXX | High | High | 0xFEFE | Start-of-Frame word |
| SOF2 | High | Low | 0xID00 + 0x00FT | High | Low | 0xID00 + 0x00FT | SP IDentifier (Geographical Address) - upper byte Frame Type – lower byte |

Table 5 shows the SOF2 bit assignment. The upper byte carries the Sector Processor ID. The lower byte defines the Frame Content format. If bits 00 to 04 are set then the corresponding blocks are present in the frame content. Here the HD stands for the Header, OB – for the Output Block, and IB – for the Input Block. There can be only one Header and one Output Block, but several Input Blocks (up to 7) in the Frame Content to have provisions for observing the neighbor bunch crossings of the trigger event. Input Blocks are Zero-Suppressed (ZS) if the ZS bit is set to 1.

Table 5: SOF2 word structure

| SOF2 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | Spare | SP ID | ZS | Spare | IB | OB | HD |

## Frame Content

The frame content immediately follows the Start-of-Frame, Table 6. The frame content is composed of the frame fields. The Header and the Data Block comprise two basic types of frame fields. The field size is always a multiple of four 16-bit words. All fields are optional, but the Header field is mandatory, if any of the Data Blocks is being transmitted. The Data Block is either an Output Block, or an Input Block. Several Input Blocks may be transmitted in the same EF for debugging purposes, as defined by the SOF2 word.

Table 6: Frame Content

| Frame Field | TX_EN | TX_ER | RX_DV/ LOS | RX_ER | Comment |
| --- | --- | --- | --- | --- | --- |
| Header | High | Low | High | Low | Mandatory if I/O Blocks present |
| Output Block | High | Low | High | Low | Optional |
| Input Block | High | Low | High | Low | Optional |
| ------------ | High | Low | High | Low | Optional |
| Input Block | High | Low | High | Low | Optional |

Idles may intermix with the frame content data words. The DDU does not store Idles in the input FIFO, since it executes FIFO writes only on the RX_DV/LOS = High condition. There should not be too many Idles in the EF, otherwise the DDU would timeout on the event readout time and mark the current event as bad (is this true -?).

### Header

The Event Frame Header consists of eight 16-bit words, shown in Table 7. It carries the L1A related information and the SP current configuration.

Table 7: Event Frame Header

| Event Header Word # | What | Comment |
| --- | --- | --- |
| HD1 | SP Code Version | Sector Processor Code Version |
| HD2 | L1A LBC | Local Bunch Counter – 12 bits |
| HD3 | L1A LEC Low | Local Event Counter - 12 LSBs |
| HD4 | L1A LEC High | Local Event Counter - 12 MSBs |
| HD5 | SR LUT Set # | Sector Receiver Look Up Table Set # |
| HD6 | SP LUT Set # | Sector Processor PT Look Up Table Set # |
| HD7 | SP Configuration | Sector Processor Configuration bits (TBD) |
| HD8 | SP Configuration | Sector Processor Configuration bits (TBD) |

### Output Block

The Output Block carries three muon tracks, delivered to the MS on bunch crossing specified by the HD2 word. Before choosing three best tracks, the SP additionally validates the input muon stubs by comparison a 2-bit bunch crossing of each muon stub with two lower bits of the Local Bunch Counter. Normally, input muon stubs with bunch crossing mismatch would not participate in the SP decision. The results of comparison are also included in the Output Block, Table 8.

Table 8: Output Block

| Word # | What | Comment |
| --- | --- | --- |
| OB1 | ME_Out_of_Synch | ME Out-of Synch muon stubs |
| OB2 | MB_Out_of_Synch | MB Out-of Synch muon stubs |
| OB3 | MS_A Low | First muon to Muon Sorter |
| OB4 | MS_A High |  |
| OB5 | MS_B Low | Second muon to Muon Sorter |
| OB6 | MS_B High |  |
| OB7 | MS_C Low | Third muon to Muon Sorter |
| OB8 | MS_C High |  |

Bit assignments for ME_Out_of_Synch and MB_Out_of_Synch words are shown in Table 9, Table 10. If any input muon stub has been already marked with the Synch_Error bit [], the OB1 would carry a logical OR of this Synch_Error bit and the result of the bunch crossing comparison.

Table 9: ME Out_of_Synch word.

| OB1 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | 0 | 4C | 4B | 4A | 3C | 3B | 3A | 2C | 2B | 2A | 1F | 1E | 1D | 1C | 1B | 1A |

Table 10: MB Out_of_Synch word.

| OB2 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1D | 1C | 1B | 1A |

### Input Block

The Input Block can be sent in two different formats: either as a Fixed Input Block, which is composed of forty 16-bit words shown in Table 13, or as a Zero-Suppressed Input Block, which is composed only of input muon stubs with Valid Pattern bit [3] asserted. In any case the Input Block starts with a word carrying the position-coded info about valid ME muon stubs:

Table 11: ME Valid Pattern word.

| IB1 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | 0 | 4C | 4B | 4A | 3C | 3B | 3A | 2C | 2B | 2A | 1F | 1E | 1D | 1C | 1B | 1A |

The MB Valid Pattern word follows the last ME muon. The MB muon stubs are coded likewise: the MB stub pattern is valid if the stub quality > 0.

Table 12: MB Valid Pattern word.

| Bit | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 1D | 1C | 1B | 1A |

The number of 16-bit words in a Zero-Suppressed Input Block should always be a multiple of 4. This is the case if the number of valid muon stubs is odd. If it is even, two padding words 0xaa55 are added at the end of the Zero-Suppressed Input Block.

Table 13: Fixed Input Block

| Word # | What | Comment |
| --- | --- | --- |
| IB1 | ME Valid Muon Stubs | ME Valid Muon Stubs with Valid Pattern bit asserted |
| IB2 | ME_1A Low | First muon data from ME1 |
| IB3 | ME_1A High |  |
| IB4 | ME_1B Low | Second muon data from ME1 |
| IB5 | ME_1B High |  |
| IB6 | ME_1C Low | Third muon data from ME1 |
| IB7 | ME_1C High |  |
| IB8 | ME_1D Low | Forth muon data from ME1 |
| IB9 | ME_1D High |  |
| IB10 | ME_1E Low | Fifth muon data from ME1 |
| IB11 | ME_1E High |  |
| IB12 | ME_1F Low | Sixth muon data from ME1 |
| IB13 | ME_1F High |  |
| IB14 | ME_2A Low | First muon data from ME2 |
| IB15 | ME_2A High |  |
| IB16 | ME_2B Low | Second muon data from ME2 |
| IB17 | ME_2B High |  |
| IB18 | ME_2C Low | Third muon data from ME2 |
| IB19 | ME_2C High |  |
| IB20 | ME_3A Low | First muon data from ME3 |
| IB21 | ME_3A High |  |
| IB22 | ME_3B Low | Second muon data from ME3 |
| IB23 | ME_3B High |  |
| IB24 | ME_3C Low | Third muon data from ME3 |
| IB25 | ME_3C High |  |
| IB26 | ME_4A Low | First muon data from ME4 |
| IB27 | ME_4A High |  |
| IB28 | ME_4B Low | Second muon data from ME4 |
| IB29 | ME_4B High |  |
| IB30 | ME_4C Low | Third muon data from ME4 |
| IB31 | ME_4C High |  |
| IB32 | MB Valid Muon Stubs | MB Valid Muon Stub <=> MB Quality > 0 |
| IB33 | MB_1A Low | First muon data from MB1 |
| IB34 | MB_1A High |  |
| IB35 | MB_1B Low | Second muon data from MB1 |
| IB36 | MB_1B High |  |
| IB37 | MB_1C Low | Third muon data from MB1 coming in next Bunch Crossing |
| IB38 | MB_1C High |  |
| IB39 | MB_1D Low | Forth muon data from MB1 coming in next Bunch Crossing |
| IB40 | MB_1D High |  |

## End-of-Frame

The End-of-Frame (EDF) delimiter immediately follows the frame content. The EOF delimiter is composed of two 16-bit words (no Idles allowed between EOF words), Table 14:

- 5-bit Fast Monitoring data in lower byte and number of Out_of_Synch input muon stubs in upper byte.

- The Error propagation word <K30.7, K30.7> or 0xFEFE

Table 14: End-of-Frame Delimiter Structure

| Word | TX_EN | TX_ER | TXD | RX_DV/ LOS | RX_ER | RXD | Comment |
| --- | --- | --- | --- | --- | --- | --- | --- |
| EOF1 | High | Low | 0xNE00 + 0x00FM | High | Low | 0xNE00 + 0x00FM | Fast Monitoring Data and number of Synch Errors |
| EOF2 | High | High | 0xXXXX | High | High | 0xFEFE | End-of-Frame word |

The FM data is composed of 5 signals:

- SP Ready (RDY)

- SP Busy (BSY)

- SP Warning of Overflow (WOV)

- SP Synch Error or Out of Synch (SER). The two terms are used interchangeably.

- SP Error (ERR)

There are 15 ME muon stubs and 4 MB muon stubs maximum. A 5-bit Number_of_Errors field is enough to cover all cases.

Table 15: EOF1 word structure

| EOF1 | 15 | 14 | 13 | 12 | 11 | 10 | 09 | 08 | 07 | 06 | 05 | 04 | 03 | 02 | 01 | 00 |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Value | Spare | Number of Errors | Spare | ERR | SER | WOV | BSY | RDY |

Revision History

| Date | Version | Comment |
| --- | --- | --- |
| October 16, 2001 | 1.0 | Initial Release |
| October 18, 2001 | 1.1 | A lot of editing |

# Endnotes

[] Fibre Channel Physical and Signaling Interface (FC-PH), Revision 4.3, page 63 (pdf-98), available at http://www.nowhere.net/~raster/FC/fcph_43.pdf

[] Texas Instruments TLK2501 1.6 to 2.5 Gbps Transceiver

[] MPC to SP Data Format, DRAFT, October 3, 2001, 
at http://red.pnpi.spb.ru/~uvarov/tf_crate/LU-MPC_SP_Data_Format_Draft.doc