# Caltech 40 metre Interferometer

# Detector Characterisation

## SPECTRAL PROPERTIES OF THE DATA

Department of Physics

The Australian National University  (ANU)

#### Sub-group of ACIGA

Susan Scott                                                      Philip Charlton

David McClelland                                           Benjamin Evans

Bernard Whiting                                              John Sandeman

##### Data analysis sub-group came into existence six months ago

### Preliminaries

- Installed and ran GRASP on several different SGI operating systems

- Read all available 40 metre data into ANU structured Mass Data Store

- Provision of interfaces between Matlab, FRAME and GRASP codes

###### Problem of Out of Lock Data

Our analysis requires the use of "good data"

i.e.  data taken when the instrument is in lock

Use lock channel IFO_Lock?

Yes, but it's too coarse for our purposes

PROBLEM :  the interferometer is not actually in lock for all sections of the lock channel showing "in lock data"

##### Manual fix :  eliminate bad data by inspection

##### How could this process be carried out automatically?

Automatic Procedure

##### Step 1 :    Only consider data which the lock channel indicates is

"in lock"

Step 2 :    Segment this "in lock" data into blocks of equal length

e.g.  1,000 data points

Step 3 :    Compute the mean signal  i  for each block and the

associated standard deviation  i  for each block

Step 4 :    Histogram the standard deviations  i  for all the blocks

Step 5 :    Using the histogram, select suitable (non-zero) minimum

and maximum standard deviations

Step 6 :    Blocks with standard deviation lying between the

minimum and maximum are marked as good

Step 7 :    The remaining blocks are marked as bad and discarded

Objective:  to deliver code for this procedure to LIGO by June 2000

Frequency Histograms

- Use good blocks of 1,000 data points

- Pad the blocks out to 8,192 = 213 points by adding zeros

- Consider the first 550 blocks of data

- Perform a Fast Fourier Transform (FFT) on each block

- Compile the FFT data into a  array

- For each frequency:

- histogram the real part of the FFT  (50 bins)

calculate the mean and standard deviation of the sample

- histogram the imaginary part of the FFT  (50 bins)

calculate the mean and standard deviation of the sample

- Execute the same procedure for the next 550 blocks of data

- Combine with the first 550 block to compile histograms:

Likelihood Ratio as a Measure of Gaussianity

- Our samples of the real and imaginary components of the FFT for a given frequency are binned

- We can therefore assume that they are distributed multinomially, with probability pi of a point falling into bin i

The likelihood function L for a multinomial distribution is given by

k is the number of bins

ni is the number of points in bin i

is the total number of points

A likelihood ratio l is obtained by taking the ratio of L to the maximum value attainable by L as the ni’s vary

N.B.  subject to the constraint

This gives a value

Example

For 2M tosses of an unbiased coin, the likelihood of n heads is

The maximum likelihood is attained when n = M.  Hence

The likelihood ratio is used to measure the Gaussianity of binned data

- Take the probabilities pi from a normal distribution with mean  and standard deviation  :

xi is the centre of the i th bin

x  is the bin width

  and    are obtained from the frequency data

L attains its maximum at

Thus l is given by

In practice it is simpler to calculate log l

- Values of  l  close to 1 indicate a good fit to Gaussian

- For large N,  l is extremely sharply peaked

- A more useful measure of Gaussianity is given by l1/N

the N th root of  l

Work in Progress

- Speed tests on the SGI PowerChallenge

- Further measures of normality

e.g.  skew, kurtosis,  (2-statistic

- Apply line removal techniques to 40 metre data

- Use the statistical analysis techniques outlined to measure the effects of different line removal techniques

(40 metre, Glasgow)