03/25/99

P. Kumar

PHY 2054

QUIZ IX/3455

Name:______________________________________________________

- The drawing shows two perpendicular wires

which lie in the plane of the paper.  They also define the

Cartesian axes from which the distances are measured.

One wire is along the x-axis and the other along the y-axis.

The point of their crossing is the origin (0,0).  Each wire

carries a current of  5.6A.  Determine the magnitude and

direction of the net magnetic field at points (0.4m, 0.2m)

and  (-0.4m, -0.2m).

Let's consider point A = (0.4, 0.2).  Suppose the vertical wire is C and the

Horizontal wire is D.  Then the magnetic field at A due to C is

Bc=(I(2( R = 2x10-7x5.6/(0.4) = 2.8 x10-6 T(.  The magnetic field due to wire D is

Bd = 5.6 x10-6 T, coming out of the paper.  The net field at A is therefore the difference between the two, B = 2.8 x10-6 T, coming out of the paper.

At the other point B = (-0.4m, -0.2m), the field due to wire C is coming out but smaller than the field due to wire D, which is pointed in to the paper (the numbers are otherwise the same).  The net field at B is therefore B = 2.8 x10-6 T (, going in to the paper.

2.  A straight wire in a magnetic field experiences a force of 0.03N when the current in the wire is 2.7A.  What is the current in the wire when it experiences a force of .047N?

since F = IBl, F1  /F2 = I1  /I2 .   Thus I2 = I1 ( F2 / F1

= 2.7 ( .047/.03

= 4.23 A

# Text boxes

C

D