CSC Track Finder Crate Specification

Draft 1/09/2003

# Abstract

This document describes the CMS Cathode Strip Chamber (CSC) Track Finder Crate requirements. Information on crate configuration, VME and custom backplanes, inter-module communications, Clock and Control Board (CCB), Sector Processor (SP), Muon Sorter (MS) and VME Master modules is included. Positions for three Muon Port Cards (MPC) and one Device Dependent Unit (DDU) is provided for debugging purposes.

- General Description

The CSC Track Finder  (TF) crate is located in the underground counting room of the CMS Experiment. The main purpose of the Track Finder is to link trigger primitives (track segments) from individual CSC muon stations into complete tracks, measure the transverse momentum Pt and report the number and quality of tracks to the Level-1 Global Muon Trigger [1].  The TF comprises 12 SP [2], one CCB [3], one MS [4] and VME Master [5] residing in a single 21-slot 9U*400 mm VME crate. Slot assignment is shown in Figure 1. Slots 1-4 are intended for 6U modules only.

Figure 1 Track Finder crate backplane

VME Master performs an overall control, monitoring and testing of the TF modules over VME bus.  VME bus is based on J1-only version of the VME64x backplane, which utilizes 160-pin 5-row connectors. Backplane connector is Harting 02-02-160-2201 female type. PCB connector is Harting 02-01-160-2101 male right angle.

All communications between TF modules are performed over custom backplane, which will be located below J1 VME backplane. Custom backplane connectors are AMP 2-mm Z-pack male type and PCB connectors are matching female right angle ones. The number of connectors per slot and number of pins per connector vary from module to module and will be described below.

- Clock and Control Board

The Clock and Control Board distributes the system clock and other signals common to all TF modules. These signals are listed in Table 1. Timing parameters correspond to a timing of the TTCrx ASIC [6].

Table 1 CCB Signal Summary

| Signal | Bits | Source | Destination | Type | Logic | Duration |
| --- | --- | --- | --- | --- | --- | --- |
| Clock Bus |
| ccb_clock40 | 17 | TTCrx, FP,Xtal | All 17 Slots | Point-to-point | LVDS | 40 MHz |
| ccb_clock80 | 3 | QPLL on CCB | MPC1,2,3 | Point-to-point | LVDS | 80 MHz |
| ccb_clock40_enable | 1 | VME, FP | All 17 Slots | Bussed | GTLP | Pulse, n counts |
| Total | 18 |  |  |  |  |  |
| Fast Control Bus |
| ccb_cmd[5..0] | 6 | TTCrx, VME | All 17 Slots | Bussed | GTLP | Level |
| ccb_evcntres | 1 | TTCrx, VME | All 17 Slots | Bussed | GTLP | 25ns |
| ccb_bcntres | 1 | TTCrx, VME | All 17 Slots | Bussed | GTLP | 25ns |
| ccb_cmd_strobe | 1 | TTCrx, VME | All 17 Slots | Bussed | GTLP | 25ns |
| ccb_bx0 | 1 | dTTCrx, VME, FP | All 17 Slots | Bussed | GTLP | 25ns+ECL FP |
| ccb_l1accept | 1 | TTCrx, VME, FP | All 17 Slots | Bussed | GTLP | 25ns+ECL FP |
| ccb_data[7..0] | 8 | TTCrx, VME | All 17 Slots | Bussed | GTLP | Level |
| ccb_data_strobe | 1 | TTCrx, VME | All 17 Slots | Bussed | GTLP | 25ns |
| ccb_reserved[3:0] | 4 | VME | All 17 Slots | Bussed | GTLP |  |
| ccb_ready | 1 | TTCrx | All 17 slots | Bussed | GTLP | Static level |
| Total | 25 |  |  |  |  |  |
| Reload Bus |
| sp_hard_reset | 1 | dTTCrx, VME | 12 SP | Bussed | GTLP | 400ns |
| sp_cfg_done[12..1] | 12 | 12 SP | VME | Point-to-Point | GTLP | Level |
| ms_hard_reset | 1 | dTTCrx, VME | MS | Point-to-Point | GTLP | 400ns |
| ms_cfg_done | 1 | MS | VME | Point-to-Point | GTLP | Level |
| mpc_hard_reset | 1 | dTTCrx, VME | 3 MPC+DDU | Bussed | GTLP | 400ns |
| Mpc_cfg_done[3:1] | 3 | 3 MPC | VME | Point-to-Point | GTLP | Level |
| Ddu_cfg_done | 1 | DDU | VME | Point-to-Point | GTLP | Level |
| Total | 20 |  |  |  |  |  |
| L1A request lines |
| Ms_l1a_req | 1 | MS | CCB | Bussed 7 | GTLP | 25 ns |
| Sp_l1a_req | 1 | SP | CCB | Bussed | GTLP | 25 ns |
| Total | 2 |  |  |  |  |  |
| Reserved Lines |
| Ms_to_ccb[1..0] | 2 | MS | CCB | Bussed | GTLP | 25 ns |
| Sp_to_ccb[2..0] | 3 | SP | CCB | Bussed | GTLP | 25 ns |
| Ccb_to_ms[2:0] | 3 | CCB | MS | Point-to-Point | GTLP | 25 ns |
| Total | 8 |  |  |  |  |  |

  - CCB Signal Description

    - Clock Bus

Ccb_clock40 – System 40.08Mhz clock. Derived from TTCrx signal Clock40Des1. The clock source can be either Clock40Des1 or an on-board crystal (80.16Mhz divided by 2 for symmetry).

Ccb_clock80 – 80.16Mhz clock. Derived from TTCrx signal Clock40Des1 by doubling its frequency in QPLL.

Ccb_clock40_enable - Enables ccb_clock40 in SP and MS to single-step synchronous logic for debugging.

    - Fast Control Bus

Ccb_cmd[5..0] – TTC broadcast commands. Commands are binary encoded according to Table 2. Extracted from TTCrx Brcst[7..2]  lines.

Table 2 Fast Control Bus Ccb_cmd[5..0] Decoding Scheme

| Signal | Code (hex) | Description |
| --- | --- | --- |
| BX0 | 1 | Bunch Crossing Zero |
| L1 Reset | 3 |  |
| Hard_reset | 4 | Reload all FPGAs at MS and SP’s from their EPROM’s |
| SP_hard_reset | 1C | Reload SP FPGAs from EPROM |
| MS_hard_reset | 1D | Reload MS FPGAs from EPROM |
| MPC_hard_reset | ??? | Reload MPC FPGAs from EPROM |

Ccb_evcntres – Event Counter Reset. TTC broadcast command, predefined to be Brcst[1]. Event Counter Reset clears the Event Counters contained in each VME module (if any) that increment on Level 1 Accept.

Ccb_bcntres – Bunch Counter Reset. TTC broadcast command, pre-defined to be Brcst[0]. Bunch Counter Reset sets the Bunch Counters (that increment on ccb_clock40) in each VME module to a predefined state.

Ccb_cmd_strobe – indicates ccb_cmd[5..0], ccb_evcntres, ccb_bx0, ccb_bcntres and ccb_l1accept  are valid on the rising edge of ccb_clock40.

Ccb_bx0 – Bunch Crossing Zero. Decoded by CCB from Brcst[7..2], it allows Bunch Counters to start counting on the next  ccb_clock40 tick.

Ccb_l1accept – L1 Accept derived from TTCrx.

Ccb_data[7..0] – individually addressed command. Extracted by CCB from Dout[7..0]

Ccb_data_strobe – indicates that ccb_data[7..0] are valid on the rising edge of ccb_clock40.

Ccb_reserved[3:0] – bussed signals from CCB to all modules reserved for future use.

Ccb_ready – static signal indicating that TTCrx chip is working properly.

    - Reload Bus

MS_hard_reset – 400 ns pulse that reloads all FPGA logic from EPROM on MS board.

SP_hard_reset – 400 ns pulse that reloads datapath FPGA logic from EPROM on SP boards.

MS_cfg_done – FPGA “configuration done” success signal from MS logic.

SP_cfg_done – FPGA “configuration done” success signal from all SP boards.

MPC_hard_reset -- 400 ns pulse that reloads all FPGA logic from EPROM on MPC and DDU boards.

MPC_cfg_done -- FPGA “configuration done” success signal from MPC logic.

DDU_cfg_done -- FPGA “configuration done” success signal from DDU logic.

    - L1A request bus

Ms_l1a_req – L1A request from MS

SP_l1a_req – L1A request from SP

The CCB pin assignment is shown on Figure 3. It is designed to be compatible with the pin assignment of the Peripheral crate CCB, so the same board can be used. All connectors used on the MS board are AMP 100145-1 parts (female 25 rows by 5 pins).

- Sector Processor

For the list of signals delivered from Sector processor to Muon Sorter, see Error! Reference source not found. in Muon Sorter Section.

For the list of signals in the control bus from CCB see Table 1 in CCB section.

For the list of signals delivered from the Sector Receiver to the DT Track-Finder through a transition board behind the backplane, and from the DT Track-Finder to the Sector Processor through a transition board behind the backplane, see  CMS IN 2002/040 Specification of the Interface Between the DT and CSC Level-1 Track-Finders

SP pin assignment is shown on Figure 2. Connectors used on SP board are AMP 100145-1 (125 pins) and 100161-1 (55 pins).

- Muon Sorter

Muon Sorter will be receiving 80MHz data streams from 12 SP. Connection to every SP comprises 32 point-to-point backplane lines. Data that is sent over these lines every 25 ns represents three best muon segments constructed by SP (see SP02 to MS Data Format document). MS selects four best patterns out of 36 possible and transmits them to Global Muon Trigger crate over four parallel LVDS cables.

Pin assignment of the custom backplane connectors X1-X4 on MS slot is given in Figure 4 and Figure 5. All connectors used on the MS board are AMP 100145-1 parts (female 25 rows by 5 pins).

- VME  Master

## TBA

- Custom Backplane Electrical and Mechanical Interfaces.

- The guiding pins will be implemented on the backplane-strengthening bars. The corresponding guiding modules will be shown on the mechanical drawings (AMP partnumber 223957-1). These modules are used also for keying the boards.

- All bussed signals must NOT be terminated on daughter boards, the tracks from the connector to GTLP transceivers should be done as short as possible.

- All 40 MHz point-to-point signals must be terminated on receiving boards: 100 OHM to 1.5 V for GTLP, 100 OHM between the complementary signals for LVDS (clock), as close to the receiver as possible.

- All 80 MHz signals must be terminated on receiving boards: 50 OHM to 1.5 V for GTLP, as close to the receiver as possible.

- 1.5 V power from the backplane is provided for GTLP termination. The board designer should provide bypassing for it. MS is powered from two regulators, so there are two 1.5V inputs. The load must be distributed so that each of the regulators provides exactly one half of the total power necessary to terminate all GTLP signals (1.5V and 1.5V_1 nets on Figure 4 and Figure 5).

- All GTLP signals are sent in negative (active “low”) logic.

- SP-to-DT feed-thru connectors’ pin assignment is not defined, all pins are left unconnected on the backplane, except for ground and 3.3V power.

- VME  Interface

All TF modules in the crate are A24D16 slaves. They will use 5-bit geographical addressing to partition the available 24-bit address space. This leaves 19 bits of address space for use within each module. Pin assignment of the VME64x J1/P1 connector is given in Table 3.

Table 3 VME64x J1/P1 connector

| Pin | Row Z | Row A | Row B | Row C | Row D |
| --- | --- | --- | --- | --- | --- |
| 1 | MRP | D00 | BBSY* | D08 | VPC |
| 2 | GND | D01 | BCLR* | D09 | GND |
| 3 | MCLK | D02 | ACFAIL* | D10 | +V1 |
| 4 | GND | D03 | BG0IN* | D11 | +V2 |
| 5 | MSD | D04 | BG0OUT* | D12 | RsvU |
| 6 | GND | D05 | BG1IN* | D13 | -V1 |
| 7 | MMD | D06 | BG1OUT* | D14 | -V2 |
| 8 | GND | D07 | BG2IN* | D15 | RsvU |
| 9 | MCTL | GND | BG2OUT* | GND | GAP* |
| 10 | GND | SYSCLK | BG3IN* | SYSFAIL* | GA0* |
| 11 | RESP* | GND | BG3OUT* | BERR* | GA1* |
| 12 | GND | DS1* | BR0* | SYSRESET* | +3.3V |
| 13 | RsvBus1 | DS0* | BR1* | LWORD* | GA2* |
| 14 | GND | WRITE* | BR2* | AM5 | +3.3V |
| 15 | RsvBus2 | GND | BR3* | A23 | GA3* |
| 16 | GND | DTACK* | AM0 | A22 | +3.3V |
| 17 | RsvBus3 | GND | AM1 | A21 | GA4* |
| 18 | GND | AS* | AM2 | A20 | +3.3V |
| 19 | RsvBus4 | GND | AM3 | A19 | RsvBus11 |
| 20 | GND | IACK* | GND | A18 | +3.3V |
| 21 | RsvBus5 | IACKIN* | SERCLK | A17 | RsvBus12 |
| 22 | GND | IACKOUT* | SERDAT | A16 | +3.3V |
| 23 | RsvBus6 | AM4 | GND | A15 | RsvBus13 |
| 24 | GND | A07 | IRQ7* | A14 | +3.3V |
| 25 | RsvBus7 | A06 | IRQ6* | A13 | RsvBus14 |
| 26 | GND | A05 | IRQ5* | A12 | +3.3V |
| 27 | RsvBus8 | A04 | IRQ4* | A11 | LI/I* |
| 28 | GND | A03 | IRQ3* | A10 | +3.3V |
| 29 | RsvBus9 | A02 | IRQ2* | A09 | LI/O* |
| 30 | GND | A01 | IRQ1* | A08 | +3.3V |
| 31 | RsvBus10 | -12V | +5VSTDBY | +12V | GND |
| 32 | GND | +5V | +5V | +5V | VPC |

# References

[1]. The Track-Finding Processor for the Level-1 Trigger of the CMS Endcap Muon System. CMS IN 1999/060. Available at: ftp://cmsdoc.cern.ch/documents/99/note99_060.pdf

[2]. Merged Sector Receiver/Sector Processor Design Specification. Available at:

http://www.phys.ufl.edu/~acosta/cms/srsp_spec.doc

[3]. Clock and Control Board for the Track Finder Crate Specification.

[4]. Muon Sorter Specification.

[5]. VME Master Specification.

[6]. TTCrx Reference Manual. February 2001. Version 3.2. Available at: http://ttc.web.cern.ch/TTC/intro.html

[7]  CMS IN 2002/040 Specification of the Interface Between the DT and CSC Level-1 Track-Finders

[8] SP02 to MS Data Format document

# History

09/24/2001: Changes in Table 3. One more line is added for communication between MS and each SP.

12/17/2001: Multiple changes in all sections. Pin assignment for all modules added.

12/06/2002: Additions and fixes after the backplane is routed. This version is to be discussed.

1/9/2003: Multiple corrections suggested by Lev Uvarov

08/23/2004: 80 MHz clock for MPC positions added (A.Madorsky)

# Appendix A: Pin assignments for the daughter boards.

# Pin assignment for the boards in the Track Finder crate

- Pin assignment for Sector Processor is shown on Figure 2, for CCB on Figure 3, for Muon sorter on Figure 4 and Figure 5.

- Zpack125 on schematics is AMP part number 100145-1 (female 25 rows by 5 pins).

- Zpack55 on schematics is AMP part number 100161-1 (female 11 rows by 5 pins).

- Mechanical drawings for connector placement are available here:

http://www.phys.ufl.edu/~madorsky/TrackFinder/ms.dxf

http://www.phys.ufl.edu/~madorsky/backplane/ccb.dxf

Figure 2 SP pin assignment

Figure 3 CCB pin assignment

Figure 4 MS J2/P2 area pin assignment

Figure 5 MS J3/P3 area pin assignment

# Footnotes

Clock:        CCB distributes Clock40Des1 from the TTCrx or a crystal or FP, de-skewed separately for each slot.

TTCrx:       Signals derived unaltered by the CCB from the TTCrx chip

FP:             Signals input or output via CCB Front Panel (ECL levels)

VME:         Signals read or written via the CCB VME interface

dTTCrx:     Signals decoded by CCB from TTCrx Brcst[7..2]

hard_reset: CCB decodes separate TTC commands for sp_hard_reset, ms_hard_reset.  The TTC command "hard_reset" pulses all hard resets simultaneously.

This signal is actually point-to-point, but there is a termination for it on the backplane to provide compatibility with peripheral CCB